## Slide 1: Breakdowns cost us four times what we spend preventing them
EXECUTIVE BRIEFING · GROUP 9226, TEAM 3
What 5,000 maintenance records across 180 assets tell us, and five decisions that could recover about $22M
Notes: Open with the one-line message: we lose far more money when equipment stops than we spend keeping it running, and a handful of decisions can change that. The analysis covers 180 assets in five groups: heavy mining equipment, railway signalling, hospital equipment, oil and gas pumps, and power systems. The data is a synthetic teaching dataset, so treat the dollar figures as illustrations of the method rather than audited numbers.

## Slide 2: One dataset that links equipment condition, repair work and money
THE PROJECT
5,000
records
60
fields: 18 descriptive, 30 measured, 12 scores
180
assets across 25 sites and 4 regions
2024–26
three years of observations
Five equipment types
Heavy mining equipment, railway signalling, hospital equipment, oil and gas pumps, power systems
Our aim
Move from logging repairs after the fact to acting on risk before equipment fails
Synthetic teaching dataset (Version 1.0) built for this project; no real company records
Notes: Introduce the project in one breath. We built one dataset that connects five things that usually sit in separate systems: the condition of each machine, its breakdowns, the repair work, the people and parts used, and the money lost when it stops. It covers 5,000 records over three years for 180 assets of five kinds, in five industries: mining, railways, healthcare, oil and gas, and power infrastructure. The data is synthetic, built for teaching, so the numbers illustrate the method. The goal is to move from simply recording repairs after they happen to deciding where to act before equipment fails.

## Slide 3: The big picture: every $1 we spend on upkeep, we lose $4.54 to breakdowns
WE SPENT
$50.4M
on maintenance: technicians, spare parts and other costs
WE LOST
$228.9M
in lost production and service while equipment was down
EQUIPMENT WAS DOWN
91,074 h
across 7,597 breakdowns; about 10 years of lost operating time
Source: Group 9226 Team 3 Enterprise Dataset v1.0, 5,000 records, 2024–2026
Notes: The headline: downtime is the real cost, not maintenance. For every dollar we spend keeping equipment running, we lose about four and a half dollars when it stops. So cutting maintenance budgets to save money is usually the wrong move; spending smarter to avoid breakdowns is the right one. Overall equipment is available about 97% of the time, which sounds good, but the remaining 3% is where the $229M goes.

## Slide 4: The fleet looks healthy on average; the problems hide in the details
FLEET SCORECARD
96.8%
of planned time equipment was available
79.4%
of planned hours actually used
342 h
average running time between breakdowns
11.7 h
average time to repair
75.2%
of work orders are planned, not emergency
76.6%
of repairs fixed first time
75.8%
average deadline compliance
14.2%
of work orders overdue (backlog)
78.5 / 100 average health score
289 high-risk records
3,950 records with overdue work
Notes: These are the headline indicators from our publication. Read the top row as good news: equipment is available almost 97% of the time and runs about 342 hours between breakdowns. Three-quarters of maintenance is planned rather than emergency work. The orange numbers are the warning signs: only three-quarters of repairs meet their deadline, and 14% of work orders are overdue. 3,950 of the 5,000 records have at least one overdue work order. Averages hide the problem, which is why the rest of the deck looks at specific groups of equipment.

## Slide 5: Every number comes from the same four steps
HOW WE WORKED
1
Check the data
5,000 records, 60 fields, 180 assets. No gaps, no duplicates. Totals match the team’s published figures.
2
Group and compare
Split records into groups (approach, importance, age) and compare costs, losses and repair times.
3
Rule out other causes
Make sure groups are alike in age and importance, and test team, shift and parts delays.
4
Price the gap
Gap per unit × how many units are affected = the value of closing it.
The slides marked “How we got this number” walk through each calculation
Notes: Before the findings, explain the method once. Step 1: we checked the data was complete and that our totals match the figures already published by the team, so we all start from the same numbers. Step 2: we grouped the records, for example by maintenance approach or by how important the equipment is, and compared them. Step 3: before blaming a cause, we checked that the groups were fair to compare, for example that one group was not simply older, and we tested other explanations such as the technician team or the shift. Step 4: we priced each gap the same simple way: the difference per unit, multiplied by how many units it affects. After each finding there is a slide that shows this arithmetic.

## Slide 6: Railway signalling is the weakest group; hospital equipment the strongest
EQUIPMENT TYPES COMPARED
Equipment type | Health | Breakdowns | Hours between | Loss | High-risk
Railway signalling | 76.8 | 1,709 | 316 h | $54.3M | 86
Oil and gas pumps | 77.7 | 1,574 | 342 h | $49.6M | 77
Heavy mining equipment | 78.4 | 1,589 | 340 h | $49.7M | 63
Power systems | 79.5 | 1,387 | 351 h | $38.8M | 39
Hospital equipment | 80.3 | 1,338 | 362 h | $36.5M | 24
Failure types are evenly spread: sensor, hydraulic, mechanical, software and electrical faults each cause 19–21% of downtime, so no single fault type is the fix. Effort should target equipment type, age and condition.
Notes: This answers which assets are deteriorating. Railway signalling has the lowest health score, the most breakdowns, the shortest time between failures and the largest losses. Hospital equipment is the healthiest. Because each equipment type behaves differently, warning limits should be set per type rather than one rule for all. We also checked the five types of fault. Each accounts for about a fifth of downtime, so a traditional “fix the top fault” Pareto exercise does not help here; you would need four of the five fault types to cover 80% of downtime.

## Slide 7: Fixing equipment before it breaks costs 37% less than waiting for it to fail
FINDING 1 · HOW WE MAINTAIN
Total cost for every hour a machine runs (upkeep plus lost output)
Wait until it breaks
$163
Fixed calendar schedule
$119
Sensor-guided (predictive)
$102
Switching our “wait until it breaks” equipment to sensor-guided care would save about $22M.
Groups compared are similar in age and importance, so the gap comes from the approach itself
Notes: Three ways we look after equipment. One: wait until it breaks, then fix it. Two: service it on a fixed calendar. Three: watch its condition with sensors and step in when the readings say it is wearing out. Waiting for failure looks cheap on the maintenance budget, but those machines break far more often, so the total cost per running hour is $163 against $102 for sensor-guided care. If the equipment we currently run to failure behaved like our sensor-guided equipment, we would avoid about 660 breakdowns, 7,900 hours of downtime and roughly $22M of cost. Sensor-guided care is not more expensive; it is cheaper per hour as well. A middle option, condition checks by technicians, delivers almost exactly the same result and may be cheaper to roll out.

## Slide 8: The $22M comes from cost per running hour × hours affected
HOW WE GOT THIS NUMBER · FINDING 1
Step | Wait until it breaks | Sensor-guided
Maintenance spend | $9.85M | $10.27M
+ Lost output | $49.50M | $44.36M
= Total cost | $59.35M | $54.63M
÷ Hours running | 364,450 h | 534,522 h
= Cost per hour | $162.9 | $102.2
Saving: ($162.9 − $102.2) = $60.6 per hour × 364,450 hours = $22.1M
IS IT A FAIR COMPARISON?
Same age: both groups average 8.0–8.1 years.
Same importance: 17–18% critical in each.
Holds at every age: breakdowns are higher under “wait until it breaks” in all four age bands.
We compare per running hour because the groups run for different lengths of time
Notes: Why per hour: the sensor-guided group simply runs more hours, so comparing raw totals would be unfair. We add maintenance spend and lost output for each group, then divide by the hours it ran. Waiting until failure costs $162.9 per hour, sensor-guided care $102.2. The gap is $60.6 per hour. The run-to-failure equipment ran 364,450 hours, so closing the gap is worth 60.6 × 364,450, about $22.1M. We also checked the two groups are alike: same average age and the same share of critical equipment, and the pattern holds at every age. So the difference comes from the maintenance approach, not from older or more important machines.

## Slide 9: Our most critical equipment gets no priority, and it costs us about $15.9M
FINDING 2 · PRIORITIES
What we measured | Critical equipment | All other equipment
Technician cost per job | $2,808 (the lowest) | $2,866–$2,896
Hours to repair | 15.8 h | 10.8 h
Repair deadline missed | 71% | 50%
Money lost per breakdown record | $61,000 | $42,600
Critical machines get the same staff, the same queue and the same deadlines as everything else, so they stay down 46% longer.
Notes: Equipment is labelled by importance: critical, high, medium, low. You would expect the critical machines to be repaired first and fastest. They are not. They get slightly less technician time than low-priority equipment, sit in the same backlog, and take about 5 hours longer to fix. Because they matter most, that extra downtime costs the most: around $15.9M across the period. The fix is a management rule, not new technology: critical work goes to the front of the queue with parts and staff reserved for it.

## Slide 10: The $15.9M is the extra loss on each critical record × 862 records
HOW WE GOT THIS NUMBER · FINDING 2
Step | Critical | All others
Lost output | $52.59M | $176.29M
÷ Records | 862 | 4,138
= Loss per record | $61,015 | $42,602
Downtime ÷ breakdowns | 21,015 h ÷ 1,289 | 70,058 h ÷ 6,308
= Hours down per breakdown | 16.3 h | 11.1 h
Extra loss: ($61,015 − $42,602) × 862 records = $15.9M
WHY WE BLAME PRIORITY
Cost per hour of downtime is the same for critical and other machines (about $2,500).
So the extra loss comes entirely from longer outages, and critical jobs get the least technician spend ($2,808 per record).
“Up to” $15.9M: matching other equipment’s repair speed is the target, not a guarantee
Notes: We divided total lost output by the number of records in each group. A critical record loses $61,015 on average, everything else $42,602. The difference, $18,413, times 862 critical records is about $15.9M. To find out why, we checked the cost of each hour of downtime: it is the same for critical and other equipment, roughly $2,500 an hour. So critical machines don’t lose more per hour; they lose more because they stay down 16.3 hours per breakdown instead of 11.1. That points to how work is prioritised, which is why the action is to put critical jobs first.

## Slide 11: Missed deadlines come from how targets are set, not from slow teams
FINDING 3 · REPAIR DEADLINES
95%
4 h target
75%
8 h target
46%
12 h target
1%
24 h target
SHARE OF JOBS THAT MISSED THE DEADLINE
Every repair takes about 12 hours, whatever the deadline.
Deadlines are handed out regardless of importance: a quarter of critical jobs get a relaxed 24 h target.
54% of all jobs miss their deadline today; the target assigned explains almost all of it
Notes: Every repair job gets a deadline: 4, 8, 12 or 24 hours. Repairs take around 12 hours no matter which deadline they get, so jobs with a 4-hour deadline almost always miss it and jobs with a 24-hour deadline almost never do. The deadlines are not linked to how important the equipment is. This is a quick, free fix: give realistic deadlines based on importance. Critical equipment should get the tight deadlines plus the resources to meet them; low-importance equipment can wait 24 hours.

## Slide 12: We counted jobs whose actual repair time ran past their deadline
HOW WE GOT THIS NUMBER · FINDING 3
Deadline | Jobs | Missed | Share
4 h | 1,269 | 1,211 | 95%
8 h | 1,215 | 916 | 75%
12 h | 1,201 | 557 | 46%
24 h | 1,315 | 10 | 1%
All jobs | 5,000 | 2,694 | 54%
Average actual repair time is 11.5–11.9 h in every row: the work is the same, only the deadline changes.
WHAT WE RULED OUT
Team: all four teams miss 53–54%.
Shift: day 52%, night 56%.
Importance: 25% of critical jobs get a 24 h deadline; 23% of low-importance jobs get 4 h.
Notes: For every job we compared the hours it actually took with the deadline it was given, and counted the misses. The pattern is striking: jobs take about 12 hours whatever deadline they get, so the deadline alone decides whether it is “missed”. We then checked whether a weak team or the night shift was to blame. They are not: every team misses about the same share. And deadlines are not linked to importance: a quarter of critical jobs get the most relaxed 24-hour deadline. That is why the action is to reset deadlines by importance, not to push teams harder.

## Slide 13: After 9 years, the chance of a high-risk machine doubles every 3 years
FINDING 4 · AGEING EQUIPMENT
0%
0–3 yrs
1%
3–6 yrs
3%
6–9 yrs
9%
9–12 yrs
18%
12–15 yrs
35%
15–20 yrs
SHARE OF RECORDS RATED HIGH-RISK
Equipment over 10 years old in poor condition accounts for 63% of all high-risk cases.
Railway signalling and oil and gas pumps are the most exposed.
289 high-risk records, 6% of the total, carry $25.1M (11%) of all losses
Notes: As equipment ages it wears, and the share of machines in the high-risk category climbs fast after about year 9: 9% at 9–12 years, 18% at 12–15, and 35% beyond 15. The 289 high-risk records are only 6% of what we track but carry 11% of the losses, about $25M. The practical rule: any machine over 10 years old with a poor condition score should be inspected and either overhauled or scheduled for replacement. Half of these high-risk machines are on the wait-until-it-breaks approach, which links back to finding 1.

## Slide 14: We sorted records by age and counted how many were rated high-risk
HOW WE GOT THIS NUMBER · FINDING 4
Age | Records | High-risk | Share
0–6 years | 1,365 | 9 | 1%
6–9 years | 1,710 | 46 | 3%
9–12 years | 1,341 | 114 | 9%
12–15 years | 499 | 90 | 18%
15–20 years | 85 | 30 | 35%
The 63%: 181 of the 289 high-risk records are over 10 years old and have a condition score below 70.
WHAT “HIGH-RISK” MEANS
The dataset’s risk score combines chance of failure, physical condition, overdue work and availability.
A score above 32 is rated high-risk. That gives 289 records.
Notes: We grouped every record by the age of the equipment and counted how many were rated high-risk in each group. The high-risk label is not our opinion; it comes from the dataset’s own risk score, which blends the chance of failure, physical condition, overdue work and availability. Anything above 32 is high-risk. The share climbs from about 1% for young equipment to 35% for equipment over 15 years old. We then looked for a simple rule managers can apply: “older than 10 years and condition score under 70” catches 181 of the 289 high-risk cases, which is 63%. That rule became the inspection action.

## Slide 15: Our alarms ring for the wrong machines and stay silent for the right ones
FINDING 5 · EARLY-WARNING ALARMS
53%
of alarms are false. 140 of 263 are set off by a high-temperature rule, yet temperature does not predict breakdowns.
73%
of high-risk machines get no alarm. They sit in the milder “watch” list, so nobody acts urgently.
Fix: trigger alarms on vibration and on condition scores, the two signals that do predict failure.
Notes: Our monitoring system raises an alarm when temperature, vibration or the condition score crosses a limit. The data shows temperature and pressure have no link to breakdowns, so the temperature rule creates false alarms, mostly on mining equipment and pumps that simply run hot. Meanwhile three quarters of the truly high-risk machines are only on the watch list. Vibration and the condition score are the reliable warning signs. Re-tuning the alarm rules costs nothing and points technicians at the right machines.

## Slide 16: We tested which sensor readings actually move the chance of failure
HOW WE GOT THIS NUMBER · FINDING 5
Reading | Best 10% | Worst 10% | Useful?
Condition score | 16% | 43% | Yes
Vibration | 25% | 35% | Yes
Temperature | 29% | 30% | No
Pressure | 29% | 30% | No
Average chance of failure for records with the best and worst readings, within each equipment type
THE ALARM COUNTS
140 of 263 alarms came from the over-82 °C rule. Only 12 of those (9%) were high-risk.
Condition alarms: 35 of 53 (66%) were high-risk.
212 of 289 high-risk records were only on the watch list.
Notes: For each sensor reading we sorted the records from best to worst and compared the chance of failure for the best 10% against the worst 10%. A useful warning sign shows a big difference. Condition score goes from 16% to 43% and vibration from 25% to 35%, so both matter. Temperature and pressure barely move it, 29% to 30%, so they tell us almost nothing. Yet the alarm system has a hard temperature limit of 82 degrees, which set off 140 of the 263 alarms, and only 12 of those machines were actually high-risk. Alarms based on condition were right two times out of three. That is why we recommend alarms based on vibration and condition instead of temperature.

## Slide 17: We under-invest in spare parts for exactly the machines that matter most
FINDING 6 · SPARE PARTS
SPARE-PARTS BUDGET VS LOSSES
9¢ vs 13¢
Critical equipment gets 9 cents of spares per $1 it loses; all other equipment gets 12–13 cents.
WHEN A PART IS OUT OF STOCK
+17%
more money lost on the same kind of job, about $7,000 extra each time.
Most exposed: critical heavy mining equipment, which loses $12.71 for every $1 of spare parts.
Notes: Spare parts are cheap compared with downtime. Across the business we spend about 12 cents on spares for every dollar lost to breakdowns, but for critical equipment that drops to 9 cents. All five types of critical equipment are the five most under-stocked groups. When a needed part is missing, the same kind of job loses about 17% more money. Recommendation: bring spare-parts cover for critical equipment up to the same level as everything else, starting with heavy mining equipment.

## Slide 18: Spares spend divided by losses, and like-for-like jobs with and without a stockout
HOW WE GOT THIS NUMBER · FINDING 6
SPARES COVER
Critical: $4.71M spares ÷ $52.59M lost = 9¢ per $1
Others: $22.17M ÷ $176.29M = 13¢ per $1
Critical heavy mining: $12.82M ÷ $1.01M = $12.71 lost per $1 of spares
STOCKOUT EFFECT
Stockouts only happen on busy machines (5+ repair orders), so we compared those 446 jobs only.
84 with a stockout lost $118,478 each; 362 without lost $101,063: +17%.
Adjusting for breakdowns and age, the stockout itself adds about $7,000.
Notes: Spares cover: we divided what we spend on spare parts by what we lose to downtime, for each group. Critical equipment gets 9 cents of spares for each dollar it loses, other equipment 13 cents. Stockout effect: missing parts only happen on machines with many repair orders, so comparing them with all jobs would exaggerate the effect. We compared only the 446 busy jobs: those with a stockout lost 17% more. Some of that is because they also had more breakdowns, so we used a statistical adjustment to separate the two; the stockout on its own adds about $7,000 per job. Both numbers point the same way: stock more parts for critical equipment.

## Slide 19: One segment in six causes 44% of all losses
EQUIPMENT SEGMENTS (AI CLUSTERING)
WORN AND FAILING
44%
of losses from 16% of records. Avg 10 years old, 3 breakdowns, 43 h down; holds 177 of the 289 high-risk records.
SLOW SERVICE
18%
of losses from 22% of records. Average condition, but only 40% of deadlines met; 96 high-risk.
AGEING, WELL SERVED
30%
of losses from 32% of records. 9 years old, but 95% of deadlines met; 16 high-risk.
YOUNG AND HEALTHY
9%
of losses from 30% of records. 5 years old, condition 84/100; no high-risk records.
Use: overhaul or replace the first group, fix response times for the second, keep the last two on routine plans.
Notes: Clustering is an AI method that sorts records into groups that behave alike, without being told the groups in advance. We gave it eight measures: age, condition, vibration, breakdowns, downtime, money lost, overdue work and deadline compliance. It found four natural segments. The key one is “worn and failing”: only 16% of records but 44% of all losses and most of the high-risk cases. The second, “slow service”, is not in bad physical shape but misses most deadlines, so its fix is faster response rather than new equipment. Each segment gets a different treatment, which is far cheaper than treating the whole fleet the same way.

## Slide 20: Reliability, work orders and maintenance strategy
OUR BUSINESS QUESTIONS · 1 OF 2
Which assets are deteriorating?
Railway signalling, and anything over 10 years old in poor condition.
What predicts failure and downtime?
Condition score, age and vibration. Temperature and pressure don’t.
Where is backlog concentrated?
Nowhere in particular: 77–82% of records are overdue in every team, shift and equipment type. It’s a planning issue.
What explains repeat repairs?
Machines with several breakdowns: 12% repeat rate with one, 25–27% with two or more. Not the team or shift.
Which strategy gives the best health?
Sensor-guided (80.4) and condition checks (80.2). Waiting for failure is worst (75.3).
Where to expand sensor-guided care?
The 798 run-to-failure records first, especially railway and pumps over 10 years old.
Notes: Our publication set out twelve business questions. This slide answers the first six in one line each. Every answer comes from the analysis earlier in the deck. The backlog answer is worth stressing: overdue work is spread evenly across every team, shift, site and equipment type, which tells us it is a planning and prioritisation problem, not a staffing problem in one place. Repeat repairs follow the machine, not the technician: machines with multiple breakdowns are twice as likely to need a second visit.

## Slide 21: Cost, service and safety, and AI
OUR BUSINESS QUESTIONS · 2 OF 2
Where is our biggest money exposure?
Railway signalling ($54.3M lost) and critical equipment ($61,000 per record, 43% above the rest).
How should spare parts be prioritised?
By loss per $1 of spares: critical equipment first, heavy mining equipment at the top ($12.71).
Where is deadline compliance weakest?
Critical equipment (64%), railway signalling (74%), and sites 25, 13 and 10.
What needs immediate escalation?
The 58 records that are both critical and high-risk. All 3 safety incidents were on run-to-failure equipment.
Which signals give early warning?
Condition score, vibration, age and maintenance approach.
How do predictions become work?
Priority = failure chance × cost of downtime × importance, sorted into a weekly work queue.
Notes: The remaining six questions. Money exposure is highest in railway signalling and in critical equipment. Spare parts should be funded where each dollar protects the most output, which puts critical heavy mining equipment first. Deadline compliance is weakest for critical equipment, which links back to the random deadlines finding. For escalation, 58 records are both critical and high-risk, and almost all of them miss their deadlines. On safety, there were only 3 incidents, all on run-to-failure equipment. The last answer explains how AI output turns into action: each machine gets a priority score combining how likely it is to fail, how much its downtime costs and how important it is, and the work queue is sorted by that score every week.

## Slide 22: Each action targets the cause we found, not the symptom
HOW WE SET THE ACTIONS · STEP 1
Problem | Cause the data points to | Action | How we valued it
High cost per hour | Run-to-failure machines break 66% more often | Move them to sensor-guided or condition checks | Cost gap × hours = $22M
Critical machines down longer | No priority rule; same staff and queue | Critical jobs first, staff and parts reserved | Loss gap × records = $15.9M
54% missed deadlines | Deadlines set at random, not slow teams | Set deadlines by importance | Misses by deadline
High-risk machines | Age over 10 plus poor condition | Inspect, overhaul or replace | Rule catches 63%
Wrong alarms | Alarm on temperature, which doesn’t predict failure | Alarm on vibration and condition | 140 false alarms removed
Stockout losses | Critical spares under-funded | Raise critical spares cover | +17% loss avoided
Notes: This slide shows the logic from problem to action. For each problem we asked: what does the data say is causing it, and what did we rule out? For example, missed deadlines are not caused by slow teams, because every team misses about the same share; they are caused by the way deadlines are assigned. So the action changes how deadlines are set rather than pushing teams harder. Each action is then valued with the arithmetic from the earlier “How we got this number” slides. The 66% figure: run-to-failure equipment has 4.57 breakdowns per 1,000 running hours against 2.76 for sensor-guided equipment.

## Slide 23: We ordered them by cost to start, speed and strength of evidence
HOW WE SET THE ACTIONS · STEP 2
Action | Cost to start | Speed | Evidence | When
Deadlines by importance | None | Days | Strong (5,000 jobs) | Day 1–30
Critical jobs first | None | Weeks | Strong (862 records) | Day 1–30
Re-tune alarms | None | Days | Strong (263 alarms) | Day 1–30
Inspect old, poor-condition machines | Low | Weeks | Strong (289 cases) | Day 1–30
Move to sensor-guided care | Medium | Months | Strong (798 records) | Day 31–90
Top up critical spares | Medium | 1–3 months | Moderate (84 stockouts) | Day 31–90
AI risk model and dashboards | Higher | A quarter | Tested on sample data | Q2 onward
Shaded rows carry the largest dollar value; they wait only because they need budget and preparation
Notes: Once we had the actions, we decided the order with three questions. How much does it cost to start? How quickly does it take effect? How strong is the evidence, meaning how many records support it? Rule changes that cost nothing, work in days and rest on thousands of records go first. Actions that need budget, like monitoring equipment or extra spare parts, come in months two and three, even though the sensor-guided switch has the biggest dollar value. The AI model comes last: it tested well, picking out 86% of high-risk cases early, but it was built on teaching data and needs the asset records fixed before it can be trusted on real equipment.

## Slide 24: Five decisions we ask you to approve
# | Decision | What it’s worth
1 | Move “wait until it breaks” equipment to sensor-guided care | About $22M saved
2 | Put critical equipment at the front of every repair queue | Up to $15.9M of losses
3 | Set repair deadlines by equipment importance | Fixes most of the 54% missed
4 | Inspect every machine over 10 years old in poor condition | Covers 63% of high-risk cases
5 | Re-tune alarms and stock spares for critical machines | 140 fewer false alarms; 17% less loss on stockouts
The savings overlap, so they should not be added together. Decisions 2–4 cost almost nothing to start.
Notes: This is the slide to leave on screen during discussion. Each decision ties back to one finding. Be clear that the savings overlap: moving equipment to sensor-guided care and prioritising critical machines partly fix the same losses, so the honest headline is “around $22M or more”, not the sum of the column. Decisions 2, 3 and 4 are management rules that need no new spending, which makes them easy first wins.

## Slide 25: Quick, free fixes first; new technology after it has proven itself
FIRST 30 DAYS
Change the rules
Deadlines by importance
Critical jobs first
Switch off false temperature alarms
Clean up asset records
DAYS 31–90
Change how we maintain
Move run-to-failure machines to condition checks
Top up critical spare parts
Extra checks on repeat-failure machines
NEXT QUARTER
Add AI and dashboards
Risk-warning model that flags 86% of high-risk cases early
Five Power BI dashboards
Humans approve every action
Notes: The order matters. The first month is about rules that cost nothing: deadlines, priorities and alarm settings. The second and third months change how we maintain equipment and top up spare parts. Only after that do we add the AI risk-warning model and dashboards. In testing, the model picked out 86% of high-risk cases by looking at just the top 10% of machines it flagged. People still make the final call on every repair.

## Slide 26: Risk prediction works today; other uses need cleaner data first
AI APPLICATIONS · TESTED ON THE PROJECT DATA
AI use | What it does | What our test showed
Failure / risk classification | Flags machines likely to become high-risk | Finds 86% of cases in its top 10% of alerts
Asset clustering | Groups machines that behave alike | 4 segments; one holds 44% of losses
Intervention recommendation | Ranks jobs by risk × cost × importance | Ready as a weekly work queue
Downtime and cost estimate | Predicts hours and money lost | Explains 74% of downtime once breakdowns are logged
Repeat-repair and overdue prediction | Warns which jobs will need a second visit or run late | Repeat: fair. Overdue: weak, a planning issue
Anomaly detection | Spots unusual sensor patterns | Useful only when condition and age are added
Remaining-life and trend forecasts | Estimates time to failure; forecasts health and workload | Needs a permanent asset ID; 2024–26 trend is flat
Notes: The publication proposed several AI uses, and we tested each on the project data. Shaded rows are ready now. The risk classifier is the standout: if technicians check only the 10% of machines it rates riskiest, they catch 86% of the real high-risk cases. Clustering produced the four segments on the earlier slide. The recommendation engine turns the model output into a sorted work list. Downtime and cost estimates become accurate once the breakdown has been logged at triage, explaining about three-quarters of the variation in downtime. Predicting overdue work is weak, which confirms that overdue work comes from planning, not from the machines. Remaining-life prediction needs a permanent ID per machine, and the health score and workload stayed flat from 2024 to 2026, so the forecast is simply “steady” for now. All tests were trained on 2024–2025 data and checked on 2026 data, the way they would be used in real life.

## Slide 27: Five dashboards, one for each decision-maker
POWER BI DASHBOARDS
Dashboard | For | Key measures | Answers
1. Fleet health | Executives | Availability, health, risk, utilisation | Where is the fleet weakest?
2. Reliability and failure | Reliability team | Time between breakdowns, repair time, downtime | What fails, where and why?
3. Work-order performance | Maintenance | Backlog, overdue, fixed first time, deadlines | Are we doing the right work on time?
4. Cost and lost output | Finance and operations | Maintenance cost, losses, stockouts, lead time | Where does the money go?
5. Predictive risk | Asset and risk leaders | Failure chance, priority score, health | What should we fix next?
All five share filters for date, equipment type, site, importance, strategy, team and risk, and every total ties back to the dataset.
Asset key for Power BI: Asset_ID & "-" & Asset_Class (900 unique keys; see appendix)
Notes: These are the five Power BI dashboards from the publication, each built for one audience. Executives get the fleet health view, reliability engineers the failure view, maintenance managers the work-order view, finance the cost view, and asset and risk leaders the predictive view with the AI priority queue. Shared filters mean that selecting, say, railway signalling at Site 25 updates every page at once. All totals reconcile with the dataset, so the numbers in this deck and in the dashboards will match.

## Slide 28: Predictions only create value when they become timely, funded and accountable work
CONCLUSION
Every AI recommendation is reviewed and approved by a person, tested on data it has not seen, explained in plain reasons and monitored over time.
GROUP 9226 · TEAM 3
Ahmed Fawzy Mohamed Rashed · Ahmed Abd Elhakam Abd Elfattaah Zaian · Khaled Abdelnasser Morsi Amer · Malak Philippe Sadek Reiad · Ali Elraey
Data Analytics for AI Business · Graduate School of Business, Arab Academy for Science, Technology and Maritime Transport
Notes: Close with the publication’s conclusion. The data and the AI tell us where to act, but value only appears when a prediction becomes a work order that is scheduled on time, has the budget and parts it needs, and has someone accountable for it. The governance principles from our publication: models are tested on data they haven’t seen, they explain their reasons, they are monitored, and a person always authorises the work. Thank the audience and open for questions.

## Slide 29: Three data points we handled before building the dashboards
APPENDIX · DATA HOUSEKEEPING
1
Asset IDs repeat across equipment types, so we created a combined key: Asset_ID + “-” + Asset_Class (for example AST-001-Industrial Pump). This gives 900 unique keys for the dashboards. A real system would use a permanent asset-register ID to track each machine’s full life.
2
The health score leaves out failure risk and backlog, and penalises machines that only had routine service. We recommend re-weighting it.
3
$9.2M of maintenance cost sits outside labour and parts. We report it as “other costs” so totals still match.
Notes: Backup slide for data questions. First, the asset ID: in this dataset the same ID is reused for different kinds of equipment, so we built a combined key from the ID and the equipment type. That makes every key unique for Power BI and gives 900 asset keys, each with about 5 or 6 records. Be honest if asked: even with this key, a record’s site and age can change from one record to the next, because the data is synthetic. It works for reporting but not for following one real machine through its life; a live system would use a permanent asset-register number. Second, the health score formula leaves out failure risk and overdue work and gives a lower score to machines that only had routine service, so we recommend re-weighting it. Third, about 18% of maintenance cost is not labour or parts; we show it as “other costs” so all totals reconcile.